## Slide 1: Project 2 - Can you hear a reservoir?
Malvin Varpe & Torgrim Odde

## Slide 2: Agenda
Introduction
Governing Equation & Transformation
Ex 1: Steady-State Solution
Ex 2: Implicit Transient Solver
Ex 3: Comparison to Line-Source Solution
Solver Performance & Scaling
Ex 4: Well test matching
Project limitations & Alternatives
Conclusions

## Slide 3: Introduction
Objective: Model radial pressure in a reservoir
Project structured into 4 exercises
  Steady state solution
  Time dependent solution
  Accuracy & performance
  Well test data fitting
Notes: Objective:
  To Model pressure behavior in a radial reservoir using both analytical (line-source) and numerical (finite-difference) approaches, and verify numerical accuracy and performance through comparison to theory and well test data
Motivation:
  Pressure behavior is important for understanding reservoir performance, estimating permeability and production strategies
  Numerical methods allow us to model realistic cases beyond what analytical solutions can do
Problem basis:
  Single-phase flow in a homogenous, isotropic reservoir with constant properties. Flow toward a vertical well
Approach:
  Derive and solve steady-state pressure equation and transient pressure equations
  Validate numerical solver vs analytical line-source (Theis) solution
  Analyze solver performance for difference methods
  Fit model parameters to real well test data
Key methods:
  Finite difference discretization in space and time
  Implicit time stepping to ensure numerical stability
  Different linear solvers (dense, sparse, Thomas)
  Curve fitting to connect simulations to field data
End goal:
  Confirm theoretical accuracy and extract reservoir parameters from actual data

## Slide 4: Governing Equation & Transformation
Radial diffusivity equation
Logarithmic coordinate transform
Simplifies operator to a constant-coefficient second derivative in y
Notes: Task foundation:
  The entire project builds on the radial diffusivity equation (hydraulic diffusivity)
Transformation:
  To simplify the Partial Differential Equation, the project uses logarithmic coordinate which converts the radial operator into a constant-coefficient second derivative
  Simplifies the discretization and improves numerical stability and accuracy!
Boundary conditions:
  Inner boundary y=yw (specified flux)
  Outer boundary y=ye (fixed pressure)

## Slide 5: Ex 1: Steady State Solution
Analytical solution for steady-state pressure
Lazy vs not-so-lazy BC at
  Lazy:
  Not-so-lazy: Ghost extrapolation (second order)
Truncation and boundary errors
Notes: Exercise objectives:
  Derive analytical solution for steady-state pressure
  Construct discrete time lazy BC with N = 4
  Compute truncation error and boundary error order
  Verify error scaling numerically
Theory:
  Steady state implication
  Lazy boundary condition (first order accuracy)
  Not-so-lazy boundary, derived from Taylor expansion (second order accurate)
Implementation in our project:
  Finite difference interior stencil, lazy and not-so-lazy boundary treatment in ‘PressureSolver’
  Analytical solution used as reference
Limitations:
  Only valid for constant properties and steady flow
  Not-so-lazy still second order, but not exact for higher complexity problems

## Slide 6: Steady State Error Behavior
Lazy BC ->
Not-so-lazy BC -> (and exact for linear solution)
Convergence verified manually
Notes: Exercise objective:
  Quantify truncation error and verify error order numerically
Theory:
  Interior truncation error
  Lazy boundary domination (first order global error)
  Not-so-lazy boundary eliminates this leading term
Implementations:
  System solver for multiple N values
  Error evaluated at fixed physical radius to ensure consistency
Results:
  Lazy BC error slope ~-1 in log-log plot
  Not-so-lazy bc slope ~0 (round-off limited – exact match!)
  Confirms theoretical expectations

## Slide 7: Ex 2: Implicit Transient Solver
Fully implicit time stepping of diffusivity equation
Discretization gives tridiagonal system per timestep
Matrix structure of N = 4
Advantages: Stable for large
Notes: Exercise objectives:
  Derivate matrix system for N=4
  Show actual numerical matrix for given parameters
  Implement a general simulator
Theory:
  Implicit backward Euler (discretized)
  Unconditionally stable and suitable for stiff problems
Implementation:
  ‘build_tridiagonal_matrix’ creates coefficient matrix
  Solver supports multiple linear solution strategies
Results:
  Matrix matches theoretical coefficients
  Solver converges for any ∆t due to implicit scheme
Limitations:
  First order in time
  Early time accuracy depends on ∆t choice

## Slide 8: Implicit Transient Solver Code

## Slide 9: Ex 3: Comparison to Line-Source Solution
Numerical vs analytical
  Discretization effect at early times
  Excellent match at intermediate times
  Boundary effects at late times
Increasing N improves early/intermediate accuracy
Increasing grid resolution improves accuracy
Notes: Exercise objective:
  Compare numerical solution to analytical line-source solution (Theis) for transient flow
    Theis represents infinite-acting reservoir
    Theis is valid until pressure front reaches boundary
Time regimes:
  Early times:
    Pressure change is limited to near the wellbore (transient zone)
  Intermediate times:
    Reservoir behaves infinite-acting (semilog plot becomes linear – grey area on graph)
  Late times:
    Pressure disturbance reaches outer boundary r=re and behavior deviates from Theis curve
Results:
  Numerical drawdown match the analytical Theis solution very well in the intermediate time region
    At early times, the small deviations are caused by time discretization and startup effects
    At late times, numerical curve flatten while analytical solution continues to decline
      The Theis does not include boundaries
Grid refinement:
  When increasing number of grid cells (N), match improves
    Spatial convergence (finer discretization leads to lower numerical error)
Performance:
  Three linear solvers
    Dense (NumPy)
    Sparse (SciPy)
    Thomas algorithm
      For small N, all perform similarly.
      For large N, Thomas algorithm is the fastest – but we expected a bigger change from SciPy
Learning point:
  Confirms solver accuracy and efficiency
    Solvers behave as theory predicts in different flow regimes
Graph:
  Shows pressure drawdown response over time for different grid sizes and radii
    Drawdown (difference in pressure −Δp=pi​−p(r,t))
  Intermediate time:
    Numerical solution:
      Constant slope
    Analytical (Theis) solution:
      Constant slope
    Why
      Pressure front is still inside reservoir (infinite-acting radial flow), so no change
  Late time:
    Numerical solution:
      Curve bends upward and flatten out toward steady-state
    Analytical (Theis) solution:
      Declining at a faster rate for all radii
    Why:
      Numerical solution reaches the outer boundary re and approaches steady-state profile
      Analytical assumes infinite reservoir, so will decrease infinitely

## Slide 10: Solver Performance & Scaling
Solvers
  Dense (NumPy) -> Cubic scaling
  Sparse (SciPy) -> Better at mid range N
  Thomas algorithm -> Linear scaling, best overall
Notes: Exercise objective:
  Visualization of 3 solvers; dense (NumPy), sparse (SciPy) and Thomas algorithm
Implementation:
  Timing across multiple N and timesteps
  Logged average runtime
Results on graphs:
  For small N, all methods similar (overhead dominates)
  Around N~200, SciPy overtakes NumPy
  Around N~200 Thomas is fastest
  Consistent with theoretical complexity
    Expected Thomas to be way faster than SciPy for large N

## Slide 11: Ex 4: Well Test Matching
Observed well pressure data loaded from well_bhp.dat
Conversion to SI units
Scatter plot of well pressure vs time
Deriving a formula
Notes: Exercise objective:
  Load well test pressure data
  Convert units to SI
  Scatter plot of well pressure vs time
  Derive formula for pw in terms of p0 (well block)
Theory:
  Observed data shows early drawdown
  Intermediate linear semilog region
  Late time stabilization (boundary-dominated flow)
  Neumann BC at well gives dp/dy = α
  Taylor over half-cell gives pw ~p0 – Δy/2 * α
Implementation:
  ‘pandas’ for reading ‘well_bhp.dat’
  Unit conversion psi -> SI
  Scatter plot for inspection
  ‘well_pressure_from_block()’ computes for each timestep
    Used for matching with well test data
Results:
  Data aligns with expected pressure decline curve shape
  Late-time plateau indicates boundary reached
  Accurate approximation of well pressure for comparison with measurements

## Slide 12: Matching Numerical Model to Field Data
Parameter fitting
Curve fit between measured data, numerical well pressure and Theis solution
Interpretation
  Early/intermediate match: Infinite acting
  Late plateau time: Boundary reached
  Line source keeps declining (no boundary)
Notes: Exercise objective:
  Fit parameters k, pi and re to data
  Compare data, numerical solution, and Theis solution on log-time plot
Theory:
  Parameter effects:
    K; slope of semilog line
    Pi; vertical offset
    Re; late-time stabilization onset
  Line-source keeps declining; numerical plateaus at boundary
Implementation
  ‘scipy.optimize.curve_fit’ to find best fit parameters
  Simulated well pressure vs measured
  Analytical theis computed with fitted parameters
Results:
  Early/intermediate match is good for both line-source and numerical
  Numerical curve levels off at late time (boundary felt)
  Fitted parameters consistent with expected behavior)

## Slide 13: Reservoir Volume from Fitted
Based fitting on
Assumes homogenous porosity and water saturation = 1
Notes: Exercise objective:
  Calculate total water volume for fitted re
Theory:
  V = ϕπ(re2​−rw2​)h
    Assuming porosity ϕ (phi) and fully water saturated
Implementation:
  Simple calculation using fitted re in SI units
Results:
  Reservoir volume derived
  Meaningful value consistent with late-time pressure
  Assumes full saturation

## Slide 14: Project Limitations and Alternatives
Assumptions
  Homogenous reservoir
  No skin or wellbore storage
  Fully implicit (1st order time)
Alternatives
  Higher order BC
  Pre factored sparse solver
  More complex boundary condition
Notes: Homogenous reservoir: Reservoir does not change over time
No skin or wellbore storage: No fluid expansion in the wellbore (storage) and no near-wall damage/stimulation which will affect (skin)

## Slide 15: Conclusions
Analytical solution and numerical solution are consistent
Boundary conditions control global accuracy
Implicit scheme is stable and flexible
Solver performance matches theoretical scaling
Well test data fitted successfully
Reservoir volume estimated from fitted parameters
Notes: Overall:
  Project integrates theory, numerical models and real data into a modeling workflow for radial flow in a reservoir
  We see that theory and simulations are consistent
  The project demonstrates accuracy and computational efficiency of chosen numerical method.
Exercise 1:
  Analytical steady-state solution derived
  We show how boundary condition choice affects error order
    Lazy BC gives first order error
    Not-so-lazy BC gives second order error
      exact match to analytical solution
Exercise 2:
  We built a robust implicit transient solver
  We verify the stability and matrix structure
Exercise 3:
  Numerical solution matches Theis in intermediate times and correctly deviates at late times when boundary is felt (as expected)
  Solver timing confirm theoretical performance
    Thomas algorithm offers best performance at large N
      Although, expected better results/larger difference from SciPy
Exercise 4:
  Real well test data successfully fitted for k, pi and re
  Numerical model reproduces real well behavior including boundary effects at late times
  Reservoir volume captured from fitted data